Setting up an IoT
Session 2: Micropython and
Hardware access
Uli Raich
Formally CERN, Geneva, Switzerland

---
The WeMos D1 mini CPU card
ESP32
ESP8266
Cost: 2.21 Euros
Cost: 4.10 Euros

---
CPU Pinout
ESP8266
ESP32

---
CPU pinouts for reference

---
Meaning of pins
- GPIO: General Purpose Input Output. Drives a single digital line which can be programmed input or output
- SCL/SDA: The I2C bus:
  a 2 wire bus interfacing sensors or actuators to the CPU
- SCL,MISO,MOSI,SS: SPI
  the Serial Peripheral Interface. Used fast communication with external device

---
The pinout

---
How to program the processor
Several development tools are available:
- ESP_IDF: The official Espressif development tool.
  Include a gcc compiler for the ESP8266 and the ESP32
- The Arduino IDE
  Needs extensions for these processors and the different CPU boards
- MicroPython
See: https://docs.espressif.com/projects/esp-idf/en/latest/
Micro USB connector

---
Flashing the code

---
esptool
- esptool is called from the Makefiles in ESP-IDF
- esptool is used when we upload code from the Arduino IDE to the processor flash
- esptool is used when the Micropython IDE uPyCraft installs Micropython onto the processor flash
In the above cases the use of esptool is hidden to us. We can however also execute esptool directly.

---
How to write a Micropython program?
First we need a Micropython interpreter!
You find the sources here:
https://github.com/micropython/micropython/
In the repository you find ports for the ESP8266 and the ESP32.
In order to compile the code you need the ESP-IDF and its cross compilers
The code compiles into a binary file (firmware-combined.bin) which contains a boot loader and the interpreter.
This binary must be uploaded and flashed.
For documentation of the ESP8266 port of Micropython look at
https://docs.micropython.org/en/latest/esp8266/tutorial/index.html

---
How to communicate with the Micropython interpreter?
We use a serial connection passing through the micro USB connection.
As soon as we connect the processor card to the PC we see the UART bridge and a new device: dev/ttyUSB0 is created.
This device is used to communicate with the Micropython REPL.

---
What is REPL?

---
The communication tools
minicom
The simplest tool is just a serial terminal emulator like minicom:
You see the command prompt and you can interact with Micropython. But … how to upload scripts?

---
ampy

---
IDE for Micropython uPyCraft

---
uPyCraft
uPyCraft is a rather complete Integrate Development Environment (IDE) which lets you
- Access the REPL
- Create directories on the Micropython file system
- Upload scripts
- Syntax check scripts
- Run scripts
- Install MicroPython on your processor board

---
Flashing MicroPython
This has already been done for you! However, it is easy if you want to do it at home with a new processor board.
Compiling a new version of Micropython is substantially harder but also perfectly possible.

---
uPyCraft(2)
uPyCraft is based on QT4 and is available for Linux, Windows and Mac. It is written in PyQt4 the Python language binding to Qt4.
The Linux version did not work for me
I found a version based on PyQt5 (new version of QT) which was even worse.
I tried to correct as much as I could to make the PyQt5 version usable on Linux:
https://github.com/uraich/uPyCraft-Qt5

---
Thonny

---
Thonny (2)
Thonny is an IDE for Python which has provisions for Micropython.
Under Tools → Options button you can select the type of Python interpreter you intend to us.

---
IoT Hello World program
A “Hello World” program, just printing “Hello World” on the screen does not look very exciting.
However, this is generally used to verify that the infrastructure
Compiler, linker, downloader, flash program
are working correctly
In embedded systems printing can be quite complex and a blinking LED is used instead.

---
Switching on and of a LED
The ESP8266 and the ESP32 have a “user LED” connected to GPIO 2.
How do we control this LED?
- Define that the LED is connected to GPIO 2
- Program this pin as output
- Write a logic 1 to the pin to switch it on
- Write a logic 0 to the pin to switch it off
The logic state may be inverted if the LED is active low

---
Micropython hardware functions

---
The machine.Pin class

---
Switch le LED on, version 1
… and there was light!

---
Switch the LED on version 2

---
The blinking LED in Micropython

---
Changing the light intensity
The LED is connected to a digital line which can only be set to 0 or Vcc. How can we change the light intensity and dim the LED?
The light intensity depends on the average current flowing through the LED. The answer is PWM: pulse width modulation.

---
PWM in Micropython

---
Our PWM implementation

---
The WS2812B LED
A more complex LED:
- rgb LED used in LED chains.
- each ws18b12 contains the 3 colored LEDs and a controller.
- Can be cascaded and individually addressed, depending on its position in the chain
- Needs precise timing
- To use it we pass through the neopixel library built into MicroPython

---
WS2812B timing
For all the details on the ws2812b look at
https://cdn-shop.adafruit.com/datasheets/WS2812B.pdf
24 bit of colour data puts
224 colours at your disposal

---
Cascading the WS2812B

---
Using the neopixel library

---
… and our code
We have a single
neopixel connected to
GPIO pin 4 (ESP8266)
or
GPIO pin 21 (ESP32)
This code works on both
CPUs!

---
The I2C bus
Quite a number of sensors in the WeMos D1 sensor shield collection use the I2C bus:
- SHT30 temperature and humidity sensor
- DS1307 real time clock
- The BMP180 barometric pressure and temperature sensor

---
The physical bus
The CPU (master) connects to the sensors (slaves) through
2 digital lines:
- SCL: the clock
- SDA: the data

---
I2C start and stop sequence
When the master want to talk to the slave it issues a start sequence
It terminates the transfer with a stop sequence

---
I2C data transfer
Data is transmitted 8 bits at a time followed by an acknowledge bit.
If acknowledge is low, transfer ok, otherwise: send stop sequence

---
I2C addressing
When talking to a slave the master sends a seven bit address followed by a read/write bit
This allows to access at most 128 devices

---
I2C write sequence
- Send start sequence
- Send I2C address and R/W bit low
- Send internal register number
- Send data byte
- Optionally send further data bytes
- Send stop sequence

---
I2C read cycle
- Send start sequence
- Send slave address with R/W low
- Send address of internal register
- Send a start sequence again
- Send slave address with R/W high
- Read data byte
- Send stop sequence

---
The SHT30
The SHT30 is a digital temperature and humidity sensor based on the I2C bus
Here is its data sheet.
Temperature precision: +- 0.3 °C
Relative humidity: +- 3 %
Works on 2.4V – 5.5 V

---
Scanning the I2C bus

---
A look at the SHT30 driver
The SHT30 driver

---
Reading out the SHT30

---
Results from the SHT30

---
WeMos D1 mini sensor and actuator shields (1)
ssd1306 46x64 OLED display
push button
ws2812b rgb LED
dht11 temperature and
humidity sensor
8x8 LED matrix
ds18b20 digital thermometer

---
Wemos D1 mini sensor and actuator shields (2)
temperature and humidity
sensor
data logger and RTC
buzzer
Triple base
prototype board

---
The data logger
The data logger features a DS1307 Real Time Clock (RTC) backed up by a battery
An SD card socket also provided.
This allows to store large amounts of data locally
The RTC keeps the time and measurements can be supplied with a time tag
Programs to set and read the RTC are provided.
One of the programs setting the RTC gets the time from and NTP server such that manual specification of the current date and time are not needed.
https://github.com/uraich/MicroPython_IoTDemos/tree/master/drivers/ds1307

---
Pinouts of Shields

---
The pushbutton shield
A simple push button
connected to
GPIO 0 (ESP8266)
Or
GPIO17 (ESP32)

---
DS18B20 shield
A digital thermometer
using the Dallas
1-wire bus

---
SSD1306 48x64 OLED display
This one is also an I2C device
It provides 48*64 pixels and allows to
- Write a few characters of text
- Do simple graphics
The ssd1306 class inherits from the
framebuf class included in Micropython such that all drawing methods of the framebuf are available for drawing:
https://docs.micropython.org/en/latest/library/framebuf.html
For an example see:https://github.com/uraich/MicroPython_IoTDemos/tree/master/drivers/oled

---
The DHT11 shield
The DHT11 is a digital temperature
and relative humidity sensor. It uses
a proprietary protocol of
communication with its controlling
host implemented in the
dht.DHT11 class

---
The LED matrix
The LED matrix has 8x8 LEDs on it, which can individually be switched on or off.
In addition to the mled class which takes care of the communication between the host and the device and which has classes to clear the display, set a pixel on or off and to change the brightness,
I wrote a class matrix which takes a number 0..64 and lights this number of LEDs starting from bottom left

---
The buzzer
This shield implements a passive buzzer.
A passive buzzer takes a frequency (an active buzzer takes a signal level) and produces a sound at this frequency.
This means that the frequency can be changed and a tune can be played.
In
https://github.com/uraich/MicroPython_IoTDemos/tree/master/drivers/buzzer
you will find a program interpreting songs on RTTTL (Ring Tone Text Transfer
Language) and playing these on the buzzer
A small song library is also provided

---
The prototype module
This is a home build module featuring a photo-resistor measuring the light intensity impinging on it.
It provides an analogue value converted to digital by the ADC on the WeMos D1 CPU
Please note that the ESP8266 has a single 10 bit ADC while the ESP32 has 3 12 bit ADCs. A MUX provides up to 18 analogue channels
The light intensity can be changed with an LED

---
The triple base
This module allows to easily stack a rather larger number of shields to a sandwich.
Make sure however that the GPIO lines used by the modules do not clash!

---
Exercises
Now it is up to
You
to work!