Digital to Analogue Conversion
Lecture 10
Uli Raich
UCC semester 2017/2018

---
Analogue versus digital
Up to now we only treated digital signals:
- on/off for the LEDs
- on/off to read the LED state
- Powering or not powering coils to generate magnetic fields in a stepping motor
However:
The world is mostly analogue:
- Temperatures are changing continuously and not in steps
- Pressure is an analogue value
- Distance, time, current, resistance … are all analogue values

---
Converting from digital to analogue
Since our computer is a digital device we must
- Convert digital values to analogue voltage levels
  Digital to Analogue Conversion (DAC)
- … and we must convert external analogue values to digital
  Analogue to Digital Conversion (ADC)

---
Digital to analogue conversion
A digital to analogue converter does not really convert into a continuous waveform
Since we have digital values as a base, there will be steps in the output waveform
The size of these steps depends on the resolution of the DAC
What is the smallest step a 12 bit DAC can produce on a 0..5V scale?

---
Can we smooth the output signal?
Yes, it is possible to smooth out these steps.
We need a low-pass filter, which filters out high frequencies (the abrupt steps we have in the output signal) and lets pass only slower transitions.
When looking carefully at the output of our sine generator you will also see these steps. In this case however they come from the limited number of sine values (100) we calculate. To improve the resolution we would have to increase the number of samples and the frequency with which we send these values to the DAC.

---
How does a DAC work?
If you want to know more about DAC technology (and you should!) have a look at this excellent tutorial, from which I have copied the above illustration.

---
The MCP4725 12 bit DAC
As a demo device we bought the MCP4725 DAC
This is a 12 bit DAC which can be accesses by the I2C bus
Here is its data sheet

---
The I2C bus
The I2C bus is an industrial standard 2 wire bus using a data (SDA) and a clock (SCL) line.
Adding Vcc and Gnd we need a mere 4 wires to connect an I2C device to the Raspberry Pi cobbler
The I2C bus was invented by Philips

---
Typical I2C connections

---
Open drain signals
Open drain signals mean that you can pull a line down but you cannot set it to a high level.
If nobody pulls the line down, then it is pulled up by a pull-up resistor to Vcc level.
Like this the contention problem is solved where one device tries to set a line to a high level, while another sets it to low, thus creating a short circuit.

---
I2C Master and slave
The I2C bus has at least one master (in our case the interface in the Raspberry Pi’s ARM processor) and several slaves
We have the following I2C slave devices:
- mcp4275 DAC
- bmp180 barometric pressure sensor
- pcf8581 8 bit ADC
- ads115 16 bit ADC
- at24c32 eeprom
- ds1307 real time clock
- mma845x accelerometer
- pcf8574 I/O expander used on the 2-line LCD display

---
I2C addressing
Since there can be several slaves on the bus there must be a means of distinguishing them through addressing:
Every I2C slave has a 7 bit address associated with it
Usually this address is determined by the manufacturer but often there are address pins on the devices allowing the user to have several devices of the same type on the bus

---
I2C buses and I2C addresses on the Raspberry Pi
The Raspberry Pi has 2 I2C buses with bus 1 being put onto the cobbler
You can find out the addresses of the I2C slaves are currently connected with the i2cdetect command

---
Initiating a I2C transfer

---
Start stop conditions
The master starts a transfer by creating a
start condition:
high to low transition on SDA while SCL is high
and ends the transfer with a
stop condition:
low to high transition on SDA while SCL is high

---
Data transmission
Data are transmitted with the SDA line stable with SCL is high

---
A write cycle
A write cycle:
After the start condition the device address. The eighth bit, the R/W bit is kept low.
The second data byte is considered the register byte and the last one the data byte
The slave acknowledges each byte transfer.

---
The read cycle
The read cycle is a bit more complex:
First the master sends the slave address with R/W set to write
Then it sends the register information.
After that another address byte is sent, this time with RW set to read
And finally the slave sends the data. The master still sends the clock but releases the SDA line allowing the slave to control it

---
I2C clock frequency
I2C bus supports different transfer speeds:
- Standard: 100 kbps
- Fast:	400 kbps
- High speed: 3.4 Mbps
pigpio seems to use the standard speed
while the Raspberry Pi can run I2C transfers of up tp 1.66 Mbps
However: you need more low level libraries or direct register access to accomplish these high speeds

---
MCP4725 Description

---
Specs of the MCP4275

---
MCP4275 registers

---
MCP4275 I2C fast write
How does the I2C write cycle look like in the MCP4275?
The MCP4275 fast write cycle only write the DAC register but not the EEPROM

---
MCP4275 normal write cycle

---
Read back the DAC data

---
Pigpio: i2c_open

---
I2C access initialization with pigpio
In addition to opening the library with pigpio_start we now also must make a connection to the I2C driver:

---
Accessing I2C with pigpio
Coming back to fast write mode, we must write 3 bytes:
- Address + R/W
- Register
- Data
The register byte contains also the high 4 bits on the 12 bit DAC data word

---
i2c_write_byte_data
The pigpio library provides a function
This means we have to split our 12 bit DAC data into 2 parts: The highest 4 bits go into i2c_reg, the lower 8 bits into bVal

---
Writing the DAC value, an example
dacValue is a short, while reg and value are unsigned char

---
DAC performance
There are a number of criteria which characterize the performance of a DAC
- Its resolution or its least significant bit (lsb)
- Its settling time (maximum speed you can go)
- Its integral non-linearity or relative accuracy
- Its differential non-linearity
- Its offset error
- Its gain error ...

---
Relative accuracy

---
Differential non-linearity

---
Offset error

---
Gain error

---
Settling Time